## Slide 1: Subsystem – Motors – PWM – C API
Registers
  Four duty cycle registers
  One direction register with four direction flag bits
  One enable register, with an overall enable bit and a refresh configuration bit
Two underlying configuration functions
  void set_dir(uint64 address, bool forwards)
  void set_duty(uint64 address, uint32 duty)
  Each accesses a writable register and writes value
Eight ease-of-use functions, two for each PWM generator
  Four “set_duty” functions
  Four “set_dir” functions
  Each is for a specific generator and feeds the correct address into the underlying call
Two synchronization functions
  void set_enable(bool)
    Turns all four PWM signals on and off at once
  void reassert_enable()
    Causes the PWM generators to simultaneously ingest duty cycles without stopping

## Slide 2: Subsystem – Motors – Encoders – C API
Four encoder registers, each with a clear bit
uint32 read_encoder(uint64 address)
  Returns value from register
Four ease-of-use functions, one for each encoder
  read_encoder_A, _B, _C, _D
  Each calls the underlying read_encoder function with the correct address
void clear_encoders()
  Iterates through each register and clears it

## Slide 3: Subsystem – Sonic Sensors – C API
Each of the three sonic sensors has a set of registers
  A read register that can be polled
  An interrupt register where interrupts can be set and cleared
  An interrupt threshold register that defines the distance to trigger an interrupt
uint32_t read_sonic(uint64 addr)
  Called in three different functions that feed in an address for a specific sensor
void set_interrupt(bool enable)
  Configures interrupt flag and registers interrupt handler
void