## Slide 1: Hardware/Software Co-Design and Verification
Dr. Kaputa

## Slide 2: SoC FPGA?
SoC = CPU + FPGA

## Slide 3: SoC FPGA Architectures
What is an SoC FPGA?
  Fully Featured ARM Processor
  Programmable Logic Fabric
Why SoC?
  Reduce Board Space and Development Time
  Increased System Flexibility
  Configurable FPGA/CPU Interconnect
  Integrated Development Tool Flow
  Open Source Software Ecosystem
Xilinx Zynq-7000
  1 GHz Dualcore ARM® Cortex™-A9
Altera SoC
  1 GHz Dualcore ARM® Cortex™-A9
Microsemi Smart Fusion 2
  166 megahertz (MHz) ARM ® CortexTM-M3 processor

## Slide 4: Advanced eXtensible Interface [AXI]
Background
  Advanced Microcontroller Bus Architecture [AMBA]
  AXI is Third Generation of AMBA
  Introduced by ARM in 1996
Xilinx Zynq SoC FPGA/CPU Interconnect
  AXI4 – Address Followed by up to 256 Data Words
  AXI-Lite – Single Address, Single Word
  AXI-Stream – Unlimited Burst Transfers [non-memory mapped]
Communicating Between FPGA and CPU
  CPU
    Bare Metal => FPGA registers accessible via global memory map
    Linux => FPGA registers accessible via /dev/mem
  FPGA
    Processor values accessible via registers
CPU
FPGA
AXI
Reg 1 0x400000000
Reg 2 0x400000004
Reg N 0x400001000

## Slide 5: Xilinx Zynq SoC FPGAs
 | Zynq UltraScale + MPSoC | Zynq - 7000
Process Node | 16 nm FinFET | 28 nm
Application Core | Quadcore ARM® Cortex™-A53 MPCore™ up to 1.3GHz | Dualcore ARM® Cortex™-A9 MPCore™ up to 1GHz
Real-Time Core | Dual ARM® Cortex™-R5 MPCore™ up to 600MHz | -
GPU | Mali™-400MP up to 466MHz | -
High Speed Connectivity | 2x USB 3.0, SATA 3.0, DisplayPort, 4x Tri-mode Gigabit Ethernet, PCIe Gen2x4 | -
Logic Cells (K) | 920 [~13.6 M] | 444 [~6.6 M]
Block Ram | 4.4 MB | 3 MB
DSP Slices | 3528 | 2020
UltraRAM | 16 MB | -

## Slide 6: Algorithm Partitioning
Solution | Execution Speed | Determinism | Design Method
ARM Processor | High | Moderate | C
Soft Processor | Moderate | Moderate/High | C
HDL State-Machine | Very High | Very High | HDL
Compile Time
Floating/Fixed Point Implementation
Algorithm Sizing
Verification Methods
Expandability
Several Companies Offer IP for SoC FPGAs
C
HDL
kHz Loops -> CPU, MHz Loops -> FPGA

## Slide 7: Use Case: SD Data Logging
Requirements
  10 MB/Sec
  Deterministic
SD Interface Algorithm
  Configuration Phase
    Very Complex
    Many Scenarios
    Non-Deterministic
  Data Transfer Phase
    Deterministic
    Relatively Simple
    High Bandwidth
How Does One Architect a Solution?

## Slide 8: Hardware/Software Co-Design
SD Configuration Phase [Control Path]
  Implement in Software via C, Python, Java
  Reasoning:
    Design Method
    Compile Time
SD Data Transfer Phase [Data Path]
  Implement in HDL
  Reasoning:
    Execution Speed
    Determinism
    Expandability
Your Decision Does not have to be Final!

## Slide 9: Finite State Machine with a Datapath [FSMD]
Next-State Logic
State Register
Output Logic
Routing
Network
Functional Units
Routing Network
Data Registers
Control Signals
Internal Status
Command
Data Input
External Status
Data Output
CONTROL PATH
DATA PATH
Key Parameters for Partitioning
  Execution Speed, Determinism, Design Method, Compile Time, Floating/Fixed Point Implementation, Algorithm Sizing, Verification Methods, Expandability, Several Companies Offer IP for SoC FPGAs
How Does One Perform Verification?

## Slide 10: Traditional HDL Verification
Functional Simulation
  Mentor Modelsim
  Altera QSim
  Xilinx Isim
Verification Via Test Benches
Pros
  Can Test Corner Cases and Fault Conditions
  Can Visualize any Signal in Design
Cons
  Difficult to Interface with Control Path [CPU Algorithm]
  Bus Functional Model may not be Available
  Can Take a Long Time to Run
Unit
Under
Test
Bus Functional Model
Test Bench

## Slide 11: Hardware/Software Cross-Triggering
The Problem
  Application Software has been Debugged
  HDL has been Simulated
  The System Does not Work
The Solution
  Embedded Co-Debug with Hardware/Software Cross-Triggering
  Hardware/Software Breakpoints
Pros
  Allows for Inter-Domain synchronization. Ex. Stop CPU and FPGA Simultaneously
  Design is not Simulated, it Runs Real Time
  No Bus Functional Model is Required
  Can Test out HDL and C code as well as External Hardware
Cons
  Must Compile the HDL
  Can be Hard to Test out Corner Cases
  Can only Look at Top Level Signals
  Limited Trace Duration

## Slide 12: Integrated Logic Analyzer [ILA]
User Selectable Probe Count and Probe Width
Boolean Trigger Equations
Enabled FPGA/CPU Cross-Triggering
Up to 1024 Probes each of width from 1 to 4096 bits.
Data Capture Depth of up to 131,072 Points
HDL
Under
Test
Hardware
C
Under
Test
Hardware
ILA

## Slide 13: Virtual IO [VIO]
Peek and Poke data through JTAG Port
Designed to Replace or Augment Board level I/O and Status Indicators
  LEDs, Push Buttons
Max Frequency: 250 MHz
Custom Output Initialization