## Slide 1: Subsystem – Motors – PWM – C API
Registers
  Four duty cycle registers
  One direction register with four direction flag bits
  One enable register, with an overall enable bit and a refresh configuration bit
Two underlying configuration functions
  void set_dir(uint64 address, bool forwards)
  void set_duty(uint64 address, uint32 duty)
  Each accesses a writable register and writes value
Eight ease-of-use functions, two for each PWM generator
  Four “set_duty” functions
  Four “set_dir” functions
  Each is for a specific generator and feeds the correct address into the underlying call
Two synchronization functions
  void set_enable(bool)
    Turns all four PWM signals on and off at once
  void reassert_enable()
    Causes the PWM generators to simultaneously ingest duty cycles without stopping

## Slide 2: Subsystem – Motors – Encoders – C API
Four encoder registers, each with a clear bit
uint32 read_encoder(uint64 address)
  Returns value from register
Four ease-of-use functions, one for each encoder
  read_encoder_A, _B, _C, _D
  Each calls the underlying read_encoder function with the correct address
void clear_encoders()
  Iterates through each register and clears it

## Slide 3: Subsystem – Sonic Sensors – C API
Each of the three sonic sensors has a set of registers
  A read register that can be polled
  An interrupt register where interrupts can be set and cleared
  An interrupt threshold register that defines the distance to trigger an interrupt
uint32 read_sonic(uint64 addr)
  Called in three different functions that feed in an address for a specific sensor
void set_interrupt(bool enable)
  Configures interrupt flag and registers interrupt handler
void clear_interrupt_flag(uint64 addr)

## Slide 4: Subsystem – Gyro IMU – C API
Uses I2C instead of AXI registers
void configure_mp2000()
  Sets the configuration registers for the IMU’s gyro and accelerometer
uint16 read_gyro_x(), read_gyro_y(), read_gyro_z()
uint16 read_accel_x(), read_accel_y(), read_accel_z()
bool self_test()
  Runs the MPU-6000’s self-test diagnostic and returns a pass or failure result
Further research: using the built-in digital motion processing feature

## Slide 5: Subsystem – LEDs – C API
Three LEDs
Each has a register with three fields:
  Enable flag
  Blink flag
  Blink period (uint16)
void enable_LED_A(), enable_LED_B(), enable_LED_C()
void set_blink_A(uint16 period), set_blink_B(uint16 period), set_blink_C(uint16 period)
void enable_blink_A(), enable_blink_B(), enable_blink_C()